## Slide 1: COSC 3406 Computer Organization
Instructor: Faraz Zaidi, PhD
Email: faraz.zaidi@algomau.ca

## Slide 2
1.4 Gates, Memory Cells, Chips, and Multichip Modules

## Slide 3: Gates and Memory Cells
Gates
  Implements a simple Boolean or logical function.
  For example, AND gate
Memory Cell
  Is a device that can store one bit of data, either 1 or 0
Computers are built from these devices

## Slide 4: Gates and Memory Cells
  Data Storage
    Provided by memory cells
  Data Processing
    Provided by gates
  Data Movement
    The paths among components are used to move data from memory to memory and from memory through gates to memory
  Control
    The paths among components can carry control signals.
    Gates and Memory cells have control signals to tell them when to perform its function
    For example, for memory cells, READ or WRITE control

## Slide 5: Fundamental Computer Elements

## Slide 6: History of Computers
  Smaller
  Cheaper
  Dissipates less heat than a vacuum tube
  Is a solid state device made from silicon
  Was invented at Bell Labs in 1947
  It was not until the late 1950’s that fully transistorized computers were commercially available
Second Generation: Transistors
Notes: The first major change in the electronic computer came with the replacement of
the vacuum tube by the transistor. The transistor is smaller, cheaper, and dissipates
less heat than a vacuum tube but can be used in the same way as a vacuum tube to
construct computers. Unlike the vacuum tube, which requires wires, metal plates, a
glass capsule, and a vacuum, the transistor is a solid-state device, made from silicon.
The transistor was invented at Bell Labs in 1947 and by the 1950s had launched
an electronic revolution. It was not until the late 1950s, however, that fully transistorized
computers were commercially available. The use of the transistor defines
the second generation of computers.

## Slide 7: Table Computer Generations
Notes: It has become widely accepted to classify computers into generations based on the fundamental
hardware technology employed (Table 1.2). Each new generation is characterized
by greater processing performance, larger memory capacity, and smaller
size than the previous one.

## Slide 8: Second Generation Computers
Introduced:
  More complex arithmetic and logic units and control units
  The use of high-level programming languages
  Provision of system software which provided the ability to:
    Load programs
    Move data to peripherals
    Libraries perform common computations
Notes: The second generation saw the introduction
of more complex arithmetic and logic units and control units, the use of
high-level programming languages, and the provision of system software with the
computer. In broad terms, system software provided the ability to load programs,
move data to peripherals, and libraries to perform common computations, similar
to what modern operating systems like Windows and Linux do.

## Slide 9
Notes: It will be useful to examine an important member of the second generation: the
IBM 7094 [BELL71]. From the introduction of the 700 series in 1952 to the introduction
of the last member of the 7000 series in 1964, this IBM product line underwent
an evolution that is typical of computer products. Successive members of the product
line showed increased performance, increased capacity, and/or lower cost.
Also, over the lifetime of this series of computers, the relative speed of the
CPU increased by a factor of 50. Speed improvements are achieved by improved
electronics (e.g., a transistor implementation is faster than a vacuum tube implementation)
and more complex circuitry. For example, the IBM 7094 includes an
Instruction Backup Register, used to buffer the next instruction. The control unit
fetches two adjacent words from memory for an instruction fetch. Except for the
occurrence of a branching instruction, which is relatively infrequent (perhaps 10 to
15%), this means that the control unit has to access memory for an instruction on
only half the instruction cycles. This prefetching significantly reduces the average
instruction cycle time.
Figure 1.9 shows a large (many peripherals) configuration for an IBM 7094,
which is representative of second-generation computers. Several differences from
the IAS computer are worth noting. The most important of these is the use of data
channels . A data channel is an independent I/O module with its own processor and
instruction set. In a computer system with such devices, the CPU does not execute
detailed I/O instructions. Such instructions are stored in a main memory to be
executed by a special-purpose processor in the data channel itself. The CPU initiates
an I/O transfer by sending a control signal to the data channel, instructing it to
execute a sequence of instructions in memory. The data channel performs its task
independently of the CPU and signals the CPU when the operation is complete.
This arrangement relieves the CPU of a considerable processing burden.
Another new feature is the multiplexor , which is the central termination
point for data channels, the CPU, and memory. The multiplexor schedules access
to the memory from the CPU and data channels, allowing these devices to act
independently.

## Slide 10: History of Computers
Third Generation: Integrated Circuits
Components as transistors, resistors, and conductors can be fabricated from a semiconductor such as silicon
Many transistors can be produced at the same time on a single wafer of silicon
Transistors can be connected with a processor metallization to form circuits
Notes: A single, self-contained transistor is called a discrete component. Throughout the
1950s and early 1960s, electronic equipment was composed largely of discrete components—
transistors, resistors, capacitors, and so on. Discrete components were
manufactured separately, packaged in their own containers, and soldered or wired
together onto masonite-like circuit boards, which were then installed in computers,
oscilloscopes, and other electronic equipment. Whenever an electronic device called
for a transistor, a little tube of metal containing a pinhead-sized piece of silicon
had to be soldered to a circuit board. The entire manufacturing process, from transistor
to circuit board, was expensive and cumbersome.
These facts of life were beginning to create problems in the computer industry.
Early second-generation computers contained about 10,000 transistors. This
figure grew to the hundreds of thousands, making the manufacture of newer, more
powerful machines increasingly difficult.
In 1958 came the achievement that revolutionized electronics and started the
era of microelectronics: the invention of the integrated circuit. It is the integrated
circuit that defines the third generation of computers. In this section, we provide a
brief introduction to the technology of integrated circuits. Then we look at perhaps
the two most important members of the third generation, both of which were introduced
at the beginning of that era: the IBM System/360 and the DEC PDP-8.

## Slide 11
Key concepts in an integrated circuit
A thin wafer of silicon is divided into a matrix of small areas, each a few millimeters square.
The identical circuit pattern is fabricated in each area, and the wafer is broken up into chips.
Each chip consists of many gates and/or memory cells plus a number of input and output attachment points.
This chip is then packaged in housing that protects it and provides pins for attachment to devices beyond the chip.
A number of these packages can then be interconnected on a printed circuit board to produce larger and more complex circuits.
Notes: Figure 1.11 depicts the key concepts in an integrated circuit. A thin wafer of
silicon is divided into a matrix of small areas, each a few millimeters square. The
identical circuit pattern is fabricated in each area, and the wafer is broken up into
chips. Each chip consists of many gates and/or memory cells plus a number of input
and output attachment points. This chip is then packaged in housing that protects
it and provides pins for attachment to devices beyond the chip. A number of these
packages can then be interconnected on a printed circuit board to produce larger
and more complex circuits.

## Slide 12
Moore’s Law: Moore observed that the number of transistors that could be
put on a single chip was doubling every year and correctly predicted that this pace
would continue into the near future.
To the surprise of many, including Moore, the pace continued year after year and decade after decade. The pace slowed to a doubling every 18 months in the 1970s but has sustained that rate ever since.
Notes: Initially, only a few gates or memory cells could be reliably manufactured
and packaged together. These early integrated circuits are referred to as small scale
Integration (SSI). As time went on, it became possible to pack more and more
Components on the same chip. This growth in density is illustrated in Figure 1.12; it is
one of the most remarkable technological trends ever recorded.
This figure reflects the
famous Moore’s law, which was propounded by Gordon Moore, cofounder of Intel,
in 1965 [MOOR65]. Moore observed that the number of transistors that could be
put on a single chip was doubling every year and correctly predicted that this pace
would continue into the near future. To the surprise of many, including Moore, the
pace continued year after year and decade after decade. The pace slowed to a doubling
every 18 months in the 1970s but has sustained that rate ever since.

## Slide 13: Moore’s Law
1965; Gordon Moore – co-founder of Intel
Observed number of transistors that could be put on a single chip was doubling every year
The pace slowed to a doubling every 18 months in the 1970’s but has sustained that rate ever since
Consequences of Moore’s law:
The cost of computer logic and memory circuitry has fallen at a dramatic rate
The electrical path length is shortened, increasing operating speed
Computer becomes smaller and is more convenient to use in a variety of environments
Reduction in power and cooling requirements
Fewer interchip connections
Notes: The consequences of Moore’s law are profound:
1. The cost of a chip has remained virtually unchanged during this period of
rapid growth in density. This means that the cost of computer logic and memory
circuitry has fallen at a dramatic rate.
2. Because logic and memory elements are placed closer together on more
densely packed chips, the electrical path length is shortened, increasing
operating speed.
3. The computer becomes smaller, making it more convenient to place in a
variety of environments.
4. There is a reduction in power and cooling requirements.
5. The interconnections on the integrated circuit are much more reliable than
solder connections. With more circuitry on each chip, there are fewer interchip
connections.

## Slide 14: IBM System/360
Announced in 1964
Product line was incompatible with older IBM machines
Was the success of the decade and cemented IBM as the overwhelmingly dominant computer vendor
The architecture remains to this day the architecture of IBM’s mainframe computers
Was the industry’s first planned family of computers
  Models were compatible in the sense that a program written for one model should be capable of being executed by another model in the series
Notes: By 1964, IBM had a firm grip on the computer market with
its 7000 series of machines. In that year, IBM announced the System/360, a new
family of computer products. Although the announcement itself was no surprise, it
contained some unpleasant news for current IBM customers: the 360 product line
was incompatible with older IBM machines. Thus, the transition to the 360 would be
difficult for the current customer base. This was a bold step by IBM, but one IBM felt
was necessary to break out of some of the constraints of the 7000 architecture and
to produce a system capable of evolving with the new integrated circuit technology
[PADE81, GIFF87]. The strategy paid off both financially and technically. The 360
was the success of the decade and cemented IBM as the overwhelmingly dominant
computer vendor, with a market share above 70%. And, with some modifications
and extensions, the architecture of the 360 remains to this day the architecture
of IBM’s mainframe computers. Examples using this architecture can be found
throughout this text.
The System/360 was the industry’s first planned family of computers. The
family covered a wide range of performance and cost. The models were compatible in the sense that
a program written for one model should be capable of being executed by another
model in the series, with only a difference in the time it takes to execute.

## Slide 15: Family Characteristics
Similar or identical instruction set
Similar or identical operating system
Increasing speed
Increasing number of I/O ports
Increasing memory size
Increasing cost
Notes: The concept of a family of compatible computers was both novel and
extremely successful. A customer with modest requirements and a budget to match
could start with the relatively inexpensive Model 30. Later, if the customer’s needs
grew, it was possible to upgrade to a faster machine with more memory without
sacrificing the investment in already-developed software. The characteristics of a
family are as follows:
• Similar or identical instruction set: In many cases, the exact same set of machine
instructions is supported on all members of the family. Thus, a program that
executes on one machine will also execute on any other. In some cases, the
lower end of the family has an instruction set that is a subset of that of the top
end of the family. This means that programs can move up but not down.
• Similar or identical operating system: The same basic operating system is
available for all family members. In some cases, additional features are added
to the higher-end members.
• Increasing speed: The rate of instruction execution increases in going from
lower to higher family members.
• Increasing number of I /O ports: The number of I/O ports increases in going
from lower to higher family members.
• Increasing memory size: The size of main memory increases in going from
lower to higher family members.
• Increasing cost: At a given point in time, the cost of a system increases in going
from lower to higher family members.
How could such a family concept be implemented? Differences were achieved
based on three factors: basic speed, size, and degree of simultaneity [STEV64]. For
example, greater speed in the execution of a given instruction could be gained by
the use of more complex circuitry in the ALU, allowing suboperations to be carried
out in parallel. Another way of increasing speed was to increase the width of the
data path between main memory and the CPU. On the Model 30, only 1 byte (8 bits)
could be fetched from main memory at a time, whereas 8 bytes could be fetched at
a time on the Model 75.
The System/360 not only dictated the future course of IBM but also had a
profound impact on the entire industry. Many of its features have become standard on
other large computers.

## Slide 16: Semiconductor Memory Microprocessors
Later
Generations
LSI
Large
Scale Integration
VLSI
Very Large Scale Integration
ULSI
Ultra Large
Scale
Integration
Notes: Beyond the third generation there is less general agreement on defining generations
of computers. Table 1.2 suggests that there have been a number of later generations,
based on advances in integrated circuit technology. With the introduction
of large-scale integration (LSI), more than 1000 components can be placed on a
single integrated circuit chip. Very-large-scale integration (VLSI) achieved more
than 10,000 components per chip, while current ultra-large-scale integration (ULSI)
chips can contain more than one billion components.
With the rapid pace of technology, the high rate of introduction of new products,
and the importance of software and communications as well as hardware, the
classification by generation becomes less clear and less meaningful. In this section,
we mention two of the most important of developments in later generations.

## Slide 17: Semiconductor Memory
In 1970 Fairchild produced the first relatively capacious semiconductor memory
Chip was about the size of a single core
Could hold 256 bits of memory
Non-destructive
Much faster than core
In 1974 the price per bit of semiconductor memory dropped below the price per bit of core memory
There has been a continuing and rapid decline in memory cost accompanied by a corresponding increase in physical memory density
Developments in memory and processor technologies changed the nature of computers in less than a decade
Since 1970 semiconductor memory has been through 13 generations
Each generation has provided four times the storage density of the previous generation, accompanied by declining cost per bit and declining access time
Notes: The first application of integrated circuit technology
to computers was construction of the processor (the control unit and the arithmetic
and logic unit) out of integrated circuit chips. But it was also found that this same
technology could be used to construct memories.
In the 1950s and 1960s, most computer memory was constructed from tiny
rings of ferromagnetic material, each about a sixteenth of an inch in diameter. These
rings were strung up on grids of fine wires suspended on small screens inside the
computer. Magnetized one way, a ring (called a core) represented a one; magnetized
the other way, it stood for a zero. Magnetic-core memory was rather fast; it took as
little as a millionth of a second to read a bit stored in memory. But it was expensive,
bulky, and used destructive readout: The simple act of reading a core erased the data
stored in it. It was therefore necessary to install circuits to restore the data as soon
as it had been extracted.
Then, in 1970, Fairchild produced the first relatively capacious semiconductor
memory. This chip, about the size of a single core, could hold 256 bits of memory. It
was nondestructive and much faster than core. It took only 70 billionths of a second
to read a bit. However, the cost per bit was higher than for that of core.
In 1974, a seminal event occurred: The price per bit of semiconductor memory
dropped below the price per bit of core memory. Following this, there has been a continuing
and rapid decline in memory cost accompanied by a corresponding increase
in physical memory density. This has led the way to smaller, faster machines with
memory sizes of larger and more expensive machines from just a few years earlier.
Developments in memory technology, together with developments in processor technology
to be discussed next, changed the nature of computers in less than a decade.
Although bulky, expensive computers remain a part of the landscape, the computer has
also been brought out to the “end user,” with office machines and personal computers.
Since 1970, semiconductor memory has been through 13 generations: 1K, 4K,
16K, 64K, 256K, 1M, 4M, 16M, 64M, 256M, 1G, 4G, and, as of this writing, 8 Gb
on a single chip (1K = 210, 1M = 220, 1G = 230). Each generation has provided four
times the storage density of the previous generation, accompanied by declining cost
per bit and declining access time. Densities are projected to reach 16 Gb by 2018 and 32 Gb by 2023
[ITRS14].

## Slide 18: Microprocessors
The density of elements on processor chips continued to rise
  More and more elements were placed on each chip so that fewer and fewer chips were needed to construct a single computer processor
1971 Intel developed 4004
  First chip to contain all of the components of a CPU on a single chip
  Birth of microprocessor
1972 Intel developed 8008
  First 8-bit microprocessor
1974 Intel developed 8080
  First general purpose microprocessor
  Faster, has a richer instruction set, has a large addressing capability
Notes: Just as the density of elements on memory chips has continued
to rise, so has the density of elements on processor chips. As time went on, more
and more elements were placed on each chip, so that fewer and fewer chips were
needed to construct a single computer processor.
A breakthrough was achieved in 1971, when Intel developed its 4004. The
4004 was the first chip to contain all of the components of a CPU on a single chip:
The microprocessor was born.
The 4004 can add two 4-bit numbers and can multiply only by repeated addition.
By today’s standards, the 4004 is hopelessly primitive, but it marked the beginning of
a continuing evolution of microprocessor capability and power.
This evolution can be seen most easily in the number of bits that the processor
deals with at a time. There is no clear-cut measure of this, but perhaps the best measure
is the data bus width: the number of bits of data that can be brought into or sent
out of the processor at a time. Another measure is the number of bits in the accumulator
or in the set of general-purpose registers. Often, these measures coincide, but
not always. For example, a number of microprocessors were developed that operate
on 16-bit numbers in registers but can only read and write 8 bits at a time.
The next major step in the evolution of the microprocessor was the introduction
in 1972 of the Intel 8008. This was the first 8-bit microprocessor and was almost twice
as complex as the 4004.
Neither of these steps was to have the impact of the next major event: the introduction
in 1974 of the Intel 8080. This was the first general-purpose microprocessor.
Whereas the 4004 and the 8008 had been designed for specific applications, the 8080
was designed to be the CPU of a general-purpose microcomputer. Like the 8008, the
8080 is an 8-bit microprocessor. The 8080, however, is faster, has a richer instruction
set, and has a large addressing capability.

## Slide 19: Evolution of Intel Microprocessors
(a) 1970s Processors
Notes: About the same time, 16-bit microprocessors began to be developed. However, it
was not until the end of the 1970s that powerful, general-purpose 16-bit microprocessors
appeared. One of these was the 8086. The next step in this trend occurred in 1981,
when both Bell Labs and Hewlett-Packard developed 32-bit, single-
chip microprocessors. Intel introduced its own 32-bit microprocessor, the 80386, in 1985 (Table 1.3).

## Slide 20: Evolution of Intel Microprocessors
(b) 1980s Processors
Notes: Table 1.3 (continued)

## Slide 21: Evolution of Intel Microprocessors
(c) 1990s Processors
Notes: Table 1.3 (continued)

## Slide 22: Evolution of Intel Microprocessors
(d) Recent Processors
Notes: Table 1.3 (continued)

## Slide 23
1.5 Evolution of the Intel x86 Architecture

## Slide 24: The Evolution of the Intel x86 Architecture
Two processor families are the Intel x86 and the ARM architectures
Current x86 offerings represent the results of decades of design effort on complex instruction set computers (CISCs)
An alternative approach to processor design is the reduced instruction set computer (RISC)
ARM architecture is used in a wide variety of embedded systems and is one of the most powerful and best-designed RISC-based systems on the market
Notes: Throughout this book, we rely on many concrete examples of computer design and
implementation to illustrate concepts and to illuminate trade-
offs. Numerous systems, both contemporary and historical, provide examples of important computer
architecture design features. But the book relies principally on examples from two
processor families: the Intel x86 and the ARM architectures. The current x86 offerings
represent the results of decades of design effort on complex instruction set
computers (CISCs). The x86 incorporates the sophisticated design principles once
found only on mainframes and supercomputers and serves as an excellent example
of CISC design. An alternative approach to processor design is the reduced instruction
set computer (RISC). The ARM architecture is used in a wide variety of embedded
systems and is one of the most powerful and best-
designed RISC-based systems
on the market. In this section and the next, we provide a brief overview of these two
systems.
In terms of market share, Intel has ranked as the number one maker of microprocessors
for non-embedded systems for decades, a position it seems unlikely to
yield. The evolution of its flagship microprocessor product serves as a good indicator
of the evolution of computer technology in general.
Table 1.3 shows that evolution. Interestingly, as microprocessors have grown
faster and much more complex, Intel has actually picked up the pace. Intel used
to develop microprocessors one after another, every four years. But Intel hopes
to keep rivals at bay by trimming a year or two off this development time, and has
done so with the most recent x86 generations.

## Slide 25: Highlights of the Evolution of the Intel Product Line:
8080
World’s first general-purpose microprocessor
8-bit machine, 8-bit data path to memory
Was used in the first personal computer (Altair)
8086
A more powerful 16-bit machine
Has an instruction cache, or queue, that prefetches a few instructions before they are executed
The first appearance of the x86 architecture
The 8088 was a variant of this processor and used in IBM’s first personal computer (securing the success of Intel
80286
Extension of the 8086 enabling addressing a 16-MB memory instead of just 1MB
80386
Intel’s first 32-bit machine
First Intel processor to support multitasking
80486
Introduced the use of much more sophisticated and powerful cache technology and sophisticated instruction pipelining
Also offered a built-in math coprocessor
Notes: It is worthwhile to list some of the highlights of the evolution of the Intel product
line:
■ 8080: The world’s first general-
purpose microprocessor. This was an 8-bit
machine, with an 8-bit data path to memory. The 8080 was used in the first
personal computer, the Altair.
■ 8086: A far more powerful, 16-bit machine. In addition to a wider data path
and larger registers, the 8086 sported an instruction cache, or queue, that
prefetches a few instructions before they are executed. A variant of this processor,
the 8088, was used in IBM’s first personal computer, securing the success
of Intel. The 8086 is the first appearance of the x86 architecture.
■ 80286: This extension of the 8086 enabled addressing a 16-MB memory instead
of just 1 MB.
■ 80386: Intel’s first 32-bit machine, and a major overhaul of the product. With
a 32-bit architecture, the 80386 rivaled the complexity and power of minicomputers
and mainframes introduced just a few years earlier. This was the first
Intel processor to support multitasking, meaning it could run multiple programs
at the same time.
■ 80486: The 80486 introduced the use of much more sophisticated and powerful
cache technology and sophisticated instruction pipelining. The 80486 also
offered a built-in math coprocessor, offloading complex math operations from
the main CPU.

## Slide 26: Highlights of the Evolution of the Intel Product Line:
Pentium
Pentium Pro
Pentium II
Pentium III
Pentium 4
Core
Core 2
Intel introduced the use of superscalar techniques, which allow multiple instructions to execute in parallel
Continued the move into superscalar organization with aggressive use of register renaming, branch prediction, data flow analysis, and speculative execution
Incorporated Intel MMX technology, which is designed specifically to process video, audio, and graphics data efficiently
Incorporated additional floating-point instructions
Streaming SIMD Extensions (SSE)
Includes additional floating-point and other enhancements for multimedia
First Intel x86 micro-core
Extends the Core architecture to 64 bits
Core 2 Quad provides four cores on a single chip
More recent Core offerings have up to 10 cores per chip
An important addition to the architecture was the Advanced Vector Extensions instruction set
Notes: ■ Pentium: With the Pentium, Intel introduced the use of superscalar techniques,
which allow multiple instructions to execute in parallel.
■ Pentium Pro: The Pentium Pro continued the move into superscalar organization
begun with the Pentium, with aggressive use of register renaming, branch
prediction, data flow analysis, and speculative execution.
■ Pentium II: The Pentium II incorporated Intel MMX technology, which is
designed specifically to process video, audio, and graphics data efficiently.
■ Pentium III: The Pentium III incorporates additional floating-
point instructions: The Streaming SIMD Extensions (SSE) instruction set extension added
70 new instructions designed to increase performance when exactly the same
operations are to be performed on multiple data objects. Typical applications
are digital signal processing and graphics processing.
■ Pentium 4: The Pentium 4 includes additional floating-
point and other enhancements for multimedia.
■ Core: This is the first Intel x86 microprocessor with a dual core, referring to
the implementation of two cores on a single chip.
■ Core 2: The Core 2 extends the Core architecture to 64 bits. The Core 2 Quad
provides four cores on a single chip. More recent Core offerings have up to 10
cores per chip. An important addition to the architecture was the Advanced
Vector Extensions instruction set that provided a set of 256-bit, and then 512-
bit, instructions for efficient processing of vector data.
Almost 40 years after its introduction in 1978, the x86 architecture continues to
dominate the processor market outside of embedded systems. Although the organization
and technology of the x86 machines have changed dramatically over the decades,
the instruction set architecture has evolved to remain backward compatible with earlier
versions. Thus, any program written on an older version of the x86 architecture
can execute on newer versions. All changes to the instruction set architecture have
involved additions to the instruction set, with no subtractions. The rate of change has
been the addition of roughly one instruction per month added to the architecture
[ANTH08], so that there are now thousands of instructions in the instruction set.
The x86 provides an excellent illustration of the advances in computer hardware
over the past 35 years. The 1978 8086 was introduced with a clock speed of
5 MHz and had 29,000 transistors. A six-
core Core i7 EE 4960X introduced in 2013
operates at 4 GHz, a speedup of a factor of 800, and has 1.86 billion transistors,
about 64,000 times as many as the 8086. Yet the Core i7 EE 4960X is in only a
slightly larger package than the 8086 and has a comparable cost.

## Slide 27
1.6 Embedded Systems

## Slide 28: Embedded Systems
The use of electronics and software within a product
Billions of computer systems are produced each year that are embedded within larger devices
Today many devices that use electric power have an embedded computing system
Often embedded systems are tightly coupled to their environment
  This can give rise to real-time constraints imposed by the need to interact with the environment
    Constraints such as required speeds of motion, required precision of measurement, and required time durations, dictate the timing of software operations
  If multiple activities must be managed simultaneously this imposes more complex real-time constraints
Notes: The term embedded system refers to the use of electronics and software within a
product, as opposed to a general-purpose computer, such as a laptop or desktop
system. Millions of computers are sold every year, including laptops, personal
computers, workstations, servers, mainframes, and supercomputers. In contrast, billions
of computer systems are produced each year that are embedded within larger
devices. Today, many, perhaps most, devices that use electric power have an embedded
computing system. It is likely that in the near future virtually all such devices
will have embedded computing systems.
Types of devices with embedded systems are almost too numerous to list.
Examples include cell phones, digital cameras, video cameras, calculators, microwave
ovens, home security systems, washing machines, lighting systems, thermostats,
printers, various automotive systems (e.g., transmission control, cruise
control, fuel injection, anti-lock brakes, and suspension systems), tennis rackets,
toothbrushes, and numerous types of sensors and actuators in automated systems.
Often, embedded systems are tightly coupled to their environment. This can
give rise to real-time constraints imposed by the need to interact with the environment.
Constraints, such as required speeds of motion, required precision of measurement,
and required time durations, dictate the timing of software operations. If
multiple activities must be managed simultaneously, this imposes more complex
real-time constraints.

## Slide 29
Embedded Systems
Notes: Figure 1.13 shows in general terms an embedded system organization. In addition
to the processor and memory, there are a number of elements that differ from
the typical desktop or laptop computer:
■ There may be a variety of interfaces that enable the system to measure, manipulate,
and otherwise interact with the external environment. Embedded systems
often interact (sense, manipulate, and communicate) with external world
through sensors and actuators and hence are typically reactive systems; a reactive
system is in continual interaction with the environment and executes at a
pace determined by that environment.
■ The human interface may be as simple as a flashing light or as complicated as
real-time robotic vision. In many cases, there is no human interface.
■ The diagnostic port may be used for diagnosing the system that is being
controlled—not just for diagnosing the computer.
■ Special-purpose field programmable (FPGA), application-specific
(ASIC), or even nondigital hardware may be used to increase performance or reliability.
■ Software often has a fixed function and is specific to the application.
■ Efficiency is of paramount importance for embedded systems. They are optimized
for energy, code size, execution time, weight and dimensions, and cost.
There are several noteworthy areas of similarity to general-
purpose computer systems as well:
■ Even with nominally fixed function software, the ability to field upgrade to fix
bugs, to improve security, and to add functionality, has become very important
for embedded system, and not just in consumer devices.
■ One comparatively recent development has been of embedded system platforms
that support a wide variety of apps. Good examples of this are smartphones
and audio/visual devices, such as smart TVs.

## Slide 30: The Internet of Things (IoT)
Term that refers to the expanding interconnection of smart devices,
ranging from appliances to tiny sensors
Is primarily driven by deeply embedded devices
Generations of deployment culminating in the IoT:
  Information technology (IT)
    PCs, servers, routers, firewalls, and so on, bought as IT devices by enterprise IT people and primarily using wired connectivity
  Operational technology (OT)
    Machines/appliances with embedded IT built by non-IT companies, such as medical machinery, SCADA, process control, and kiosks, bought as appliances by enterprise OT people and primarily using wired connectivity
  Personal technology
    Smartphones, tablets, and eBook readers bought as IT devices by consumers exclusively using wireless connectivity and often multiple forms of wireless connectivity
  Sensor/actuator technology
    Single-purpose devices bought by consumers, IT, and OT people exclusively using wireless connectivity, generally of a single form, as part of larger systems
  It is the fourth generation that is usually thought of as the IoT and it is marked by the use of billions of embedded devices
Notes: The Internet of things (IoT) is a term that refers to the
expanding interconnection of smart devices, ranging from appliances to tiny sensors.
A dominant theme is the embedding of short- range mobile transceivers into a wide
array of gadgets and everyday items, enabling new forms of communication between
people and things, and between things themselves. The Internet now supports the
interconnection of billions of industrial and personal objects, usually through cloud
systems. The objects deliver sensor information, act on their environment, and, in
some cases, modify themselves, to create overall management of a larger system, like
a factory or city.
The IoT is primarily driven by deeply embedded devices (defined below).
These devices are low-bandwidth, low-repetition data-capture, and low-bandwidth
data-usage appliances that communicate with each other and provide data via user
interfaces. Embedded appliances, such as high-resolution
video security cameras, video VoIP phones, and a handful of others, require high-bandwidth
streaming capabilities. Yet countless products simply require packets of data to be intermittently
delivered.
With reference to the end systems supported, the Internet has gone through
roughly four generations of deployment culminating in the IoT:
1. Information technology (IT) : PCs, servers, routers, firewalls, and so on, bought
as IT devices by enterprise IT people and primarily using wired connectivity
2. Operational technology (OT) : Machines/appliances with embedded IT built
by non-IT companies, such as medical machinery, SCADA (supervisory control
and data acquisition), process control, and kiosks, bought as appliances by
enterprise OT people and primarily using wired connectivity
3. Personal technology: Smartphones, tablets, and eBook readers bought as IT
devices by consumers (employees) exclusively using wireless connectivity and
often multiple forms of wireless connectivity
4. Sensor/actuator technology: Single-purpose devices bought by consumers, IT,
and OT people exclusively using wireless connectivity, generally of a single
form, as part of larger systems
It is the fourth generation that is usually thought of as the IoT, and it is marked
by the use of billions of embedded devices.

## Slide 31
There are two general approaches to developing an embedded operating system (OS):
  Take an existing OS and adapt it for the embedded application
  Design and implement an OS intended solely for embedded use
Application processors
  Defined by the processor’s ability to execute complex operating systems
  General-purpose in nature
  An example is the smartphone – the embedded system is designed to support numerous apps and perform a wide variety of functions
Dedicated processor
  Is dedicated to one or a small number of specific tasks required by the host device
  Because such an embedded system is dedicated to a specific task or tasks, the processor and associated components can be engineered to reduce size and cost
Embedded
Operating
Systems
Application Processors
versus
Dedicated Processors
Notes: There are two general approaches to developing an embedded operating system
(OS). The first approach is to take an existing OS and adapt it for the embedded
application. For example, there are embedded versions of Linux, Windows, and
Mac, as well as other commercial and proprietary operating systems specialized for
embedded systems. The other approach is to design and implement an OS intended
solely for embedded use. An example of the latter is TinyOS, widely used in wireless
sensor networks. This topic is explored in depth in [STAL15].
In this subsection, and the next two, we briefly introduce some terms commonly
found in the literature on embedded systems. Application processors are defined
by the processor’s ability to execute complex operating systems, such as Linux,
Android, and Chrome. Thus, the application processor is general-purpose in nature.
A good example of the use of an embedded application processor is the smartphone.
The embedded system is designed to support numerous apps and perform a wide
variety of functions.
Most embedded systems employ a dedicated processor , which, as the name
implies, is dedicated to one or a small number of specific tasks required by the host
device. Because such an embedded system is dedicated to a specific task or tasks,
the processor and associated components can be engineered to reduce size and cost.

## Slide 32: Microprocessors vs Microcontrollers
Microprocessor: Registers, ALU, Control Unit
Microcontroller: Single chip contains processor, non-volatile memory, volatile memory, clock, I/O control unit
Notes: It is worthwhile calling out separately one of the major drivers in the proliferation
of embedded systems. The Internet of things (IoT) is a term that refers to the
expanding interconnection of smart devices, ranging from appliances to tiny sensors.
A dominant theme is the embedding of short- range mobile transceivers into a wide
array of gadgets and everyday items, enabling new forms of communication between
people and things, and between things themselves. The Internet now supports the
interconnection of billions of industrial and personal objects, usually through cloud
systems. The objects deliver sensor information, act on their environment, and, in
some cases, modify themselves, to create overall management of a larger system, like
a factory or city.
The IoT is primarily driven by deeply embedded devices (defined below).
These devices are low-bandwidth, low-repetition data-capture, and low-bandwidth
data-usage appliances that communicate with each other and provide data via user
interfaces. Embedded appliances, such as high-resolution
video security cameras, video VoIP phones, and a handful of others, require high-bandwidth
streaming capabilities. Yet countless products simply require packets of data to be intermittently
delivered.
With reference to the end systems supported, the Internet has gone through
roughly four generations of deployment culminating in the IoT:
1. Information technology (IT) : PCs, servers, routers, firewalls, and so on, bought
as IT devices by enterprise IT people and primarily using wired connectivity
2. Operational technology (OT) : Machines/appliances with embedded IT built
by non-IT companies, such as medical machinery, SCADA (supervisory control
and data acquisition), process control, and kiosks, bought as appliances by
enterprise OT people and primarily using wired connectivity
3. Personal technology: Smartphones, tablets, and eBook readers bought as IT
devices by consumers (employees) exclusively using wireless connectivity and
often multiple forms of wireless connectivity
4. Sensor/actuator technology: Single-purpose devices bought by consumers, IT,
and OT people exclusively using wireless connectivity, generally of a single
form, as part of larger systems
It is the fourth generation that is usually thought of as the IoT, and it is marked
by the use of billions of embedded devices.

## Slide 33
Notes: As we have seen, early microprocessor chips included registers, an ALU, and some
sort of control unit or instruction processing logic. As transistor density increased, it
became possible to increase the complexity of the instruction set architecture, and
ultimately to add memory and more than one processor. Contemporary microprocessor
chips, as shown in Figure 1.2, include multiple cores and a substantial amount
of cache memory.
A microcontroller chip makes a substantially different use of the logic space
available. Figure 1.15 shows in general terms the elements typically found on a microcontroller
chip. As shown, a microcontroller is a single chip that contains the processor,
non-volatile memory for the program (ROM), volatile memory for input and output
(RAM), a clock, and an I/O control unit. The processor portion of the microcontroller
has a much lower silicon area than other microprocessors and much higher energy efficiency.
We examine microcontroller organization in more detail in Section 1.6.
Also called a “computer on a chip,” billions of microcontroller units are
embedded each year in myriad products from toys to appliances to automobiles. For
example, a single vehicle can use 70 or more microcontrollers. Typically, especially
for the smaller, less expensive microcontrollers, they are used as dedicated processors
for specific tasks. For example, microcontrollers are heavily utilized in automation
processes. By providing simple reactions to input, they can control machinery,
turn fans on and off, open and close valves, and so forth. They are integral parts of
modern industrial technology and are among the most inexpensive ways to produce
machinery that can handle extremely complex functionalities.
Microcontrollers come in a range of physical sizes and processing power. Processors
range from 4-bit to 32-bit architectures. Microcontrollers tend to be much
slower than microprocessors, typically operating in the MHz range rather than the
GHz speeds of microprocessors. Another typical feature of a microcontroller is that
it does not provide for human interaction. The microcontroller is programmed for a
specific task, embedded in its device, and executes as and when required.

## Slide 34: Deeply Embedded Systems
Subset of embedded systems
Uses a microcontroller rather than a microprocessor
Is not programmable once the program logic for the device has been burned into ROM
Has no interaction with a user
Dedicated, single-purpose devices that detect something in the environment, perform a basic level of processing, and then do something with the results
Often have wireless capability and appear in networked configurations, such as networks of sensors deployed over a large area
Typically have extreme resource constraints in terms of memory, processor size, time, and power consumption
Notes: We have, in this section, defined the concept of an embedded system. A subset of
embedded systems, and a quite numerous subset, is referred to as deeply embedded
systems . Although this term is widely used in the technical and commercial
literature, you will search the Internet in vain (or at least I did) for a straightforward
definition. Generally, we can say that a deeply embedded system has a processor
whose behavior is difficult to observe both by the programmer and the user.
A deeply embedded system uses a microcontroller rather than a microprocessor, is
not programmable once the program logic for the device has been burned into ROM
(read-only memory), and has no interaction with a user.
Deeply embedded systems are dedicated, single-purpose devices that detect something in the environment,
perform a basic level of processing, and then do
something with the results. Deeply embedded systems often have wireless capability
and appear in networked configurations, such as networks of sensors deployed
over a large area (e.g., factory, agricultural field). The Internet of things depends
heavily on deeply embedded systems. Typically, deeply embedded systems have
extreme resource constraints in terms of memory, processor size, time, and power
consumption.

## Slide 35
1.7 ARM Architecture

## Slide 36: ARM
Refers to a processor architecture that has evolved from RISC design principles and is used in embedded systems
Family of RISC-based microprocessors and microcontrollers designed by ARM Holdings, Cambridge, England
Chips are high-speed processors that are known for their small die size and low power requirements
Probably the most widely used embedded processor architecture and indeed the most widely used processor architecture of any kind in the world
Acorn RISC Machine/Advanced RISC Machine
Notes: The ARM architecture refers to a processor architecture that has evolved from
RISC design principles and is used in embedded systems. Chapter 15 examines
RISC design principles in detail. In this section, we give a brief overview of the
ARM architecture.
ARM is a family of RISC-based
microprocessors and microcontrollers designed
by ARM Holdings, Cambridge, England. The company doesn’t make processors
but instead designs microprocessor and multicore architectures and licenses them
to manufacturers. Specifically, ARM Holdings has two types of licensable products:
processors and processor architectures. For processors, the customer buys the
rights to use ARM-supplied design in their own chips. For a processor architecture,
the customer buys the rights to design their own processor compliant with ARM’s
architecture.
ARM chips are high-speed
processors that are known for their small die size
and low power requirements. They are widely used in smartphones and other handheld
devices, including game systems, as well as a large variety of consumer products.
ARM chips are the processors in Apple’s popular iPod and iPhone devices,
and are used in virtually all Android smartphones as well. ARM is probably the
most widely used embedded processor architecture and indeed the most widely
used processor architecture of any kind in the world [VANC14].
The origins of ARM technology can be traced back to the British-based
Acorn Computers company. In the early 1980s, Acorn was awarded a contract by the British
Broadcasting Corporation (BBC) to develop a new microcomputer architecture
for the BBC Computer Literacy Project. The success of this contract enabled Acorn
to go on to develop the first commercial RISC processor, the Acorn RISC Machine
(ARM). The first version, ARM1, became operational in 1985 and was used for
internal research and development as well as being used as a coprocessor in the
BBC machine.
In this early stage, Acorn used the company VLSI Technology to do the actual
fabrication of the processor chips. VLSI was licensed to market the chip on its own
and had some success in getting other companies to use the ARM in their products,
particularly as an embedded processor.
The ARM design matched a growing commercial need for a high-performance,
Low-power-consumption, small-size, and low-cost
processor for embedded applications.
But further development was beyond the scope of Acorn’s capabilities.
Accordingly, a new company was organized, with Acorn, VLSI, and Apple Computer
as founding partners, known as ARM Ltd. The Acorn RISC Machine became
Advanced RISC Machines.

## Slide 37: ARM Products
Cortex-A/Cortex-A50
Cortex-R
Cortex-M
Cortex-M0
Cortex-M0+
Cortex-M3
Cortex-M4
Cortex M7
Cortex M23
Cortex M33
Notes: ARM Holdings licenses a number of specialized microprocessors and related technologies,
but the bulk of their product line is the Cortex family of microprocessor
architectures. There are three Cortex architectures, conveniently labeled with the
initials A, R, and M.
The Cortex-Aand Cortex-A50
are application processors, intended for mobile devices such as smartphones and eBook readers,
as well as consumer devices such as digital TV and home gateways (e.g., DSL and
cable Internet modems). These processors run at higher clock frequency (over
1 GHz), and support a memory management unit (MMU), which is required for full
feature OSs such as Linux, Android, MS Windows, and mobile OSs. An MMU is
a hardware module that supports virtual memory and paging by translating virtual
addresses into physical addresses; this topic is explored in Chapter 8.
The two architectures use both the ARM and Thumb-2
instruction sets; the principal difference is that the Cortex-A
is a 32-bit machine, and the Cortex-A50 is a 64-bit machine.
The Cortex-R is designed to support real-time applications, in which the
timing of events needs to be controlled with rapid response to events. They can run at
a fairly high clock frequency (e.g., 200MHz to 800MHz) and have very low response
latency. The Cortex-R includes enhancements both to the instruction set and to the
processor organization to support deeply embedded real-time
devices. Most of these
processors do not have MMU; the limited data requirements and the limited number
of simultaneous processes eliminates the need for elaborate hardware and software
support for virtual memory. The Cortex-R
does have a Memory Protection Unit
(MPU), cache, and other memory features designed for industrial applications. An
MPU is a hardware module that prohibits one program in memory from accidentally
accessing memory assigned to another active program. Using various methods, a
protective boundary is created around the program, and instructions within the
program are prohibited from referencing data outside of that boundary.
Examples of embedded systems that would use the Cortex-R
are automotive braking systems, mass storage controllers, and networking and printing devices.
Cortex-M series processors have been developed primarily for the
microcontroller domain where the need for fast, highly deterministic interrupt
management is coupled with the desire for extremely low gate count and
lowest possible power consumption. As with the Cortex-R
series, the Cortex-M architecture has an MPU but no MMU. The Cortex-M
uses only the Thumb-2 instruction set. The market for the Cortex-M
includes IoT devices, wireless sensor/actuator networks used in factories and other enterprises, automotive
body electronics, and so on.
There are currently four versions of the Cortex-M
series:
■ Cortex-M0 :
Designed for 8- and 16-bit applications, this model emphasizes low
cost, ultra low power, and simplicity. It is optimized for small silicon die size
(starting from 12k gates) and use in the lowest cost chips.
■ Cortex-M0+ :
An enhanced version of the M0 that is more energy efficient.
■ Cortex-M3 :
Designed for 16- and 32-bit applications, this model emphasizes
performance and energy efficiency. It also has comprehensive debug and trace
features to enable software developers to develop their applications quickly.
■ Cortex-M4 :
This model provides all the features of the Cortex-M3,
with additional instructions to support digital signal processing tasks.
In this text, we will primarily use the ARM Cortex-M3
as our example embedded
system processor. It is the best suited of all ARM models for general-purpose
microcontroller use. The Cortex-M3 is used by a variety of manufacturers of microcontroller
products. Initial microcontroller devices from lead partners already
combine the Cortex-M3
processor with flash, SRAM, and multiple peripherals to
provide a competitive offering at the price of just $1.

## Slide 38
Notes: Figure 1.16 provides a block diagram of the EFM32 microcontroller from Silicon
Labs. The figure also shows detail of the Cortex-M3
processor and core components.
We examine each level in turn.
The Cortex-M3 core makes use of separate buses for instructions and data.
This arrangement is sometimes referred to as a Harvard architecture, in contrast
with the von Neumann architecture, which uses the same signal buses and memory
for both instructions and data. By being able to read both an instruction and
data from memory at the same time, the Cortex-M3 processor can perform many
operations in parallel, speeding application execution. The core contains a decoder
for Thumb instructions, an advanced ALU with support for hardware multiply and
divide, control logic, and interfaces to the other components of the processor. In
particular, there is an interface to the nested vector interrupt controller (NVIC) and
the embedded trace macrocell (ETM) module.
The core is part of a module called the Cortex-M3
processor . This term is somewhat misleading, because typically in the literature, the terms core and processor
are viewed as equivalent. In addition to the core, the processor includes the
following elements:
■ NVIC : Provides configurable interrupt handling abilities to the processor. It
facilitates low-latency exception and interrupt handling, and controls power
management.
■ ETM : An optional debug component that enables reconstruction of program
execution. The ETM is designed to be a high-speed, low-power debug tool
that only supports instruction trace.
■ Debug access port (DAP) : This provides an interface for external debug
access to the processor.
■ Debug logic : Basic debug functionality includes processor halt, single-
step, processor core register access, unlimited software breakpoints, and full system
memory access.
■ ICode interface : Fetches instructions from the code memory space.
■ SRAM & peripheral interface : Read/write interface to data memory and peripheral
devices.
■ Bus matrix : Connects the core and debug interfaces to external buses on the
microcontroller.
■ Memory protection unit : Protects critical data used by the operating system
from user applications, separating processing tasks by disallowing access
to each other’s data, disabling access to memory regions, allowing memory
regions to be defined as read-only,
and detecting unexpected memory accesses
that could potentially break the system.
The upper part of Figure 1.16 shows the block diagram of a typical microcontroller
built with the Cortex-M3, in this case the EFM32 microcontroller. This
microcontroller is marketed for use in a wide variety of devices, including energy,
gas, and water metering; alarm and security systems; industrial automation devices;
home automation devices; smart accessories; and health and fitness devices. The silicon
chip consists of 10 main areas:
■ Core and memory: This region includes the Cortex-M3
processor, static RAM (SRAM) data memory, and flash memory15 for storing program instructions
and nonvarying application data. Flash memory is nonvolatile (data is not lost
when power is shut off) and so is ideal for this purpose. The SRAM stores
variable data. This area also includes a debug interface, which makes it easy to
reprogram and update the system in the field.
■ Parallel I/O ports: Configurable for a variety of parallel I/O schemes.
■ Serial interfaces: Supports various serial I/O schemes.
■ Analog interfaces : Analog-to-digital and digital-to-analog
logic to support sensors and actuators.
■ Timers and triggers : Keeps track of timing and counts events, generates output
waveforms, and triggers timed actions in other peripherals.
■ Clock management : Controls the clocks and oscillators on the chip. Multiple
clocks and oscillators are used to minimize power consumption and provide
short startup times.
■ Energy management : Manages the various low-energy
modes of operation of the processor and peripherals to provide real-time
management of the energy needs so as to minimize energy consumption.
■ Security : The chip includes a hardware implementation of the Advanced
Encryption Standard (AES).
■ 32-bit bus : Connects all of the components on the chip.
■ Peripheral bus : A network which lets the different peripheral module communicate
directly with each other without involving the processor. This supports
timing-critical operation and reduces software overhead.
Comparing Figure 1.16 with Figure 1.2, you will see many similarities and
the same general hierarchical structure. Note, however, that the top level of a
microcontroller computer system is a single chip, whereas for a multicore computer,
the top level is a motherboard containing a number of chips. Another noteworthy
difference is that there is no cache, neither in the Cortex-M3 processor
nor in the microcontroller as a whole, which plays an important role if the code or
data resides in external memory. Though the number of cycles to read the instruction
or data varies depending on cache hit or miss, the cache greatly improves the
performance when external memory is used. Such overhead is not needed for a
microcontroller.

## Slide 39: Summary
Organization and architecture
Structure and function
Brief history of computers
  The First Generation: Vacuum tubes
  The Second Generation: Transistors
  The Third Generation: Integrated Circuits
  Later generations
  The evolution of the Intel x86 architecture
Embedded systems
  The Internet of things
  Embedded operating systems
  Application processors versus dedicated processors
  Microprocessors versus microcontrollers
  Embedded versus deeply embedded systems
ARM architecture
  ARM evolution
  Instruction set architecture
  ARM products
Chapter 1
Basic Concepts and Computer Evolution
Notes: Chapter 1 summary.